## Slide 1
🏆 HARDWARE HACKATHON
SAPTHAGIRI NPS UNIVERSITY
Low Power Motion
Activated Alert Circuit
Smart Motion-Activated Power Management System with Blynk IoT Integration
Team Members
Thejas B C | Sachit N Mandre | Vivek S | Hemanth H | Shivkumar A
Section 4ECE03 • Raspberry Pi Pico 2W • MicroPython
PIR Sensor
Blynk IoT
ACS712
ZMPT101B
LCD 16x2

## Slide 2
PROBLEM STATEMENT & PROJECT OVERVIEW
⚡ PROBLEM
▶ Lights left ON unnecessarily
▶ Energy wasted in empty rooms
▶ No remote monitoring capability
▶ Manual switches are inefficient
▶ No energy usage tracking
✅ OUR SOLUTION
✔ PIR motion detection auto ON/OFF
✔ Real-time IoT dashboard via Blynk
✔ Live voltage & current monitoring
✔ Manual override with push button
✔ Energy (Wh) tracking & alerts
VS
Raspberry Pi Pico 2W • MicroPython • Blynk IoT Cloud

## Slide 3
SYSTEM ARCHITECTURE
🔧 RPi Pico 2W
MicroPython
PIR Sensor
HC-SR501
Push Button
Manual
ACS712
Current
Relay Module
2-Channel
LCD 16x2
I2C Display
ZMPT101B
Voltage
🔔 Buzzer
☁️ Blynk IoT Cloud
WiFi 2.4GHz
INPUTS
OUTPUTS

## Slide 4
HARDWARE PIN CONNECTIONS — Raspberry Pi Pico 2W
Component | Pin | Connects To | Component | Pin | Connects To
PIR HC-SR501 | VCC | VBUS (Pin 40) | Relay 2-Ch | IN1 | GP14 (Pin 19)
PIR HC-SR501 | GND | GND | Relay 2-Ch | IN2 | GP13 (Pin 17)
PIR HC-SR501 | OUT | GP15 (Pin 20) | Relay 2-Ch | VCC | VBUS (Pin 40)
LCD 16x2 I2C | VCC | 3.3V (Pin 36) | Buzzer | + | GP16 (Pin 21)
LCD 16x2 I2C | SDA | GP0 (Pin 1) | Buzzer | - | GND
LCD 16x2 I2C | SCL | GP1 (Pin 2) | Button | Leg 1 | GP18 (Pin 24)
ACS712 | VCC | 3.3V | Button | Leg 2 | GND
ACS712 | GND | GND | ZMPT101B | VCC | 3.3V
ACS712 | OUT | GP26 (ADC0, Pin 31) | ZMPT101B | GND | GND
 |  |  | ZMPT101B | OUT | GP27 (ADC1, Pin 32)
Relay CH1 NO+COM → Bulb Circuit (AC Load)

## Slide 5
CIRCUIT CONNECTION DIAGRAM
RASPBERRY Pi
PICO 2W
GP15 →PIR
GP26 →ACS
GP27 →ZMPT
3.3V
GP14→ Relay
GP16→ Buzzer
GP18→ Button
GP0/1→ LCD
📡 WiFi 2.4GHz
PIR
HC-SR501
LCD 16x2
I2C 0x27
Button
GP18
ACS712
Current
ZMPT101B
Voltage
Relay +
Bulb
Buzzer
GP16
☁️ Blynk Cloud V0-V5

## Slide 6
KEY FEATURES & FUNCTIONALITY
🚶 Motion Detection
HC-SR501 PIR with 10-sample debounce for reliable detection. Confirmed trigger needs 5/10 high reads.
💡 Auto Power Control
Relay cuts power after 30s of no motion. Active-low relay logic ensures fail-safe OFF state.
📊 Energy Monitoring
Real-time V, I, W and Wh tracking. ZMPT101B for AC voltage, ACS712 for current with noise offset.
📱 Blynk IoT Dashboard
6 virtual pins (V0–V5) pushed every 5s. Motion alerts and bulb status visible on mobile app.
🔘 Manual Override
Button toggles auto/manual mode. Manual mode bypasses PIR — user controls the bulb directly.
🖥️ LCD Status Display
16x2 I2C LCD shows live V, A, W, Wh. Scrolling status messages on motion and bulb events.
Timeout: 30s • Cooldown: 8s • Blynk update: every 5s • ADC samples: 200 per reading

## Slide 7
BLYNK IoT INTEGRATION — Virtual Pin Mapping
⚡ V0 — Voltage
Unit: Volts (V)
Pushed every 5 seconds
via batch/update API
🔌 V1 — Current
Unit: Amperes (A)
Pushed every 5 seconds
via batch/update API
💡 V2 — Power
Unit: Watts (W)
Pushed every 5 seconds
via batch/update API
📈 V3 — Energy
Unit: Wh (cumulative)
Pushed every 5 seconds
via batch/update API
🚶 V4 — Motion
Unit: 0 = None / 1 = Detected
Pushed every 5 seconds
via batch/update API
🔮 V5 — Bulb State
Unit: 0 = OFF / 1 = ON
Pushed every 5 seconds
via batch/update API
Free tier — /notify endpoint suppressed (ECONNRESET expected) | Batch update: blynk.cloud/external/api/batch/update

## Slide 8
PROGRAM FLOW — State Machine Logic
START UP
LCD Init → WiFi Connect
PIR Warmup (5s)
WAIT STATE
Light Sleep (100ms)
Listen: PIR + Button
MOTION / BUTTON
Confirmed Trigger
Bulb ON + Beep×2
MONITOR LOOP
Read V, I, W
Update LCD + Blynk
PIR ACTIVE?
If YES → reset timer
Needs 2 consec reads
TIMEOUT 30s?
Auto Mode only
Turn Bulb OFF
BUTTON PRESS?
Toggle ON/OFF
Cooldown: 8s
Energy tracked per session (Wh) → added to total_energy on each loop iteration (watts/3600)

## Slide 9
RESULTS & ACHIEVEMENTS
30s
Auto-Off Timeout
Configurable
200×
ADC Samples / Reading
For noise reduction
5s
Blynk Update Rate
Real-time IoT
6
Virtual Pin Channels
V0 through V5
✅ Key Accomplishments
Stable WiFi reconnect with ensure_wifi() fallback
Noise offset calibration for ACS712 (~4.5A bias removed)
ZMPT101B calibration constant (775) for accurate AC voltage
Light sleep (machine.lightsleep) for low power wait state
⚙️ Technical Specs
Platform: Raspberry Pi Pico 2W, MicroPython
Power: VBUS (5V) + 3.3V for sensors
LCD: I2C 0x27, 4-bit mode, 16×2 display
Network: Blynk Cloud API (batch update)
WiFi: ASSESSMENT_SNPSU • Language: MicroPython • IDE: Thonny

## Slide 10
CONCLUSION & FUTURE SCOPE
📌 Conclusion
Fully functional IoT-enabled smart lighting system
Real-time monitoring via Blynk mobile app
Accurate power measurement with calibrated sensors
Auto & manual modes for flexible operation
Low power design using light sleep
🚀 Future Scope
OLED display for richer UI
Multiple zones / multi-relay control
Data logging to SD card or cloud DB
AI-based occupancy prediction
Voice assistant integration
Thank You!
Thejas B C • Sachit N Mandre • Vivek S • Hemanth H • Shivkumar A | 4ECE03 • Sapthagiri NPS University